## Slide 1: Metals used for ships
Year 12 Chemistry - Shipwrecks

## Slide 2: Iron/Steel ships
Iron and various forms of steel are the primary metals used in the production of ships because they:
  Are relatively hard
  Are mechanically strong
  Can be worked into different shapes/structures
  Can be welded

## Slide 3: Steel (Fe + C)
Steel is an alloy in which iron is mixed with carbon and other elements in varying percentages to change its properties. The more carbon the harder and more brittle. Above1.5%, the steel is so brittle, it loses its usefulness. Addition of carbon does not reduce corrosion
% Carbon | Properties | Uses
Mild (0.2%) | Easily welded, machined and shaped (malleable) | Nails, chains, cables
Medium/Structural (0.2-0.5%) | Strong and somewhat malleable | Buildings, railways, girders, cars, ships
High (0.5-1.5%) | Hard, strong, but tends to be brittle. Resists wear. Not very malleable | Small tools (hammers, axes, scissors), blades

## Slide 4: Other steel additives
Element | Ni | Cr | Mn | Si | W | Mo | V | Al
Effect | Increase strength, ductility, resist corrosion | Increase hardness, resist wear and corrosion | Increase strength, hardness, decrease brittleness | Increase resilience, flexibility | Increase hardness at high temps | Increase strength at high temps and resists corrosion, more easily welded and less brittle | Increase strength, shock resistance | Decrease weight, Improves fatigue resistance, more easily welded
Uses | Vehicle gears, crankshafts. Found in stainless steel | Gears, axles, ball bearings, tools. Found in stainless steel | Rifle barrels, gears, axles, safes | Springs, transformers, magnets | High speed cutting tools | Gears, drive shafts, aircraft, pressure vessels | Bearings, tools, axles | Ships, electromagnets

## Slide 5: Corrosion
Corrosion is a general term that refers to the deterioration of materials reacting with chemicals. It is mostly associated with the effect of water and oxygen on metals (often on iron).
The corrosion of metals involves redox reactions where the metal is oxidised to a positive ion.

## Slide 6: Active/Passivating metals
Active metal: refers to a metal that is reactive/easily oxidised in air. This is relative (e.g. Zn is more active than Fe)
Passive metal: refers to a metal that is unreactive as it forms a protective oxide layer on its surface. E.g. Al forms a protective oxide coating Al2O3. Others include Pb, Zn, Cr.
A more active metal can be used as a “sacrificial anode” to protect a less active metal from corrosion (more about this later).

## Slide 7
The reactions of metals with oxygen, water and acids involve the metals losing electrons to form +ve metal ions.
When an atom loses one or more electrons, it is oxidised. If an atom gains electrons, it is reduced. Therefore:
Oxidation is loss of e-
Reduction is gain of e-
In any equation, there is no overall loss or gain of e-. Therefore, oxidation and reduction occur simultaneously and are known as redox reactions.
Oxidation-Reduction (REDOX)

## Slide 8: Redox reactions are a transfer of e-
Remember that redox reactions involve the transfer of electrons from one species to another
The substance that is oxidised provides e- to the substance that is reduced
In the activity series to the right, those on the top are the most easily oxidised (have lowest E0)

## Slide 9
Oxidation - Reduction
Oxidation States (some rules)
The oxidation state of a free element (i.e. not part of a compound) is zero (e.g. Zn(s), O2(g))
The oxidation state of an element in an ionic compound is equal the electrical charge on its ion. (e.g. Na+ = +1)
Oxidation states of elements in covalent compounds are calculated as if they were ionic. The most electronegative atom (closest to F in the periodic table) is assumed to gain electrons. (e.g. NH3; N = -3, H = +1)
The sum of the oxidation states of all the elements in a compound is zero.
The oxidation state of oxygen in a compound is normally -2, except for peroxides, when it is -1. (e.g. H2O2; H = 1, O = -1)
The oxidation state of hydrogen in a compound is normally +1, except for metal hydrides, when it is -1. (e.g. NaH; Na = 1, H = -1)

## Slide 10
Oxidation - Reduction
A metal reacting with acid is an example of a redox reaction. Consider the following rxn:
Zn(s) + 2HCl(aq)  ZnCl2(aq) + H2(g)
This reaction can be written as an ionic equation:
Zn(s) + 2H+(aq) + 2Cl-(aq)  Zn2+(aq) + 2Cl-(aq) + H2(g)
Note the two chloride ions that appear on both sides of the equation. These are known as spectator ions. These can be removed to give us a net ionic equation:
Zn(s) + 2H+(aq)  Zn2+(aq) + H2(g)
Which of these species has been oxidised? Which has been reduced?

## Slide 11
Oxidation - Reduction
Zn(s) + 2H+(aq)  Zn2+(aq) + H2(g)
This net ionic equation can be written as two half reactions:
Oxidation: zinc dissolves and loses electrons
Zn(s)  Zn2+(aq) + 2e- (loss of e-)
Reduction: hydrogen ions gain electrons to form H gas
2H+(aq) + 2e-  H2(g) (gain of e-)
Note that combining these two half reactions results in a balance of electrons. Try this process using sulfuric acid.

## Slide 12
Rust as a redox reaction
In all metal corrosion reactions, the metal is oxidised to form a positive metal ion (i.e. loses electrons).
The more reactive the metal, the more likely the metal is to be oxidised.
Iron is oxidised by oxygen in the presence of water to form rust. The overall reaction is:
4Fe(s) + 3O2(g) + 2H2O(l) → 2Fe2O3 . xH2O(s) (rusting)
Note: x is a value from 1-3 indicating waters of hydration

## Slide 13
Rust as a redox reaction
The two initial reactions involved in (wet corrosion)rusting are:
Fe(s) → Fe 2+(aq) + 2e– (oxidation)
and
O2(g) + 2H2O(l) + 4e– → 4OH– (aq) (reduction)
Iron(II) reacts with hydroxide to form the green precipitate, iron(II) hydroxide
Fe 2+(aq) + 2OH–(aq) → Fe(OH)2(s) (green rust)

## Slide 14
Rust as a redox reaction
Further exposure to moisture and oxygen leads to the oxidation of iron(II)hydroxide to red-brown iron(III)hydroxide
4Fe(OH)2 (s) + 2H2O(l) + O2(g) → 4Fe(OH)3(s)
Iron(III)hydroxide then dehydrates to form rust
2Fe(OH)3 (s) → Fe2O3.xH2O (s) (rust)

## Slide 15
Rusting is a destructive process

## Slide 16: Conditions affecting rust
Two conditions required for rust:
Oxygen present
Water present
Acceleration of rust can occur in:
Presence of salt
Presence of impurities
Presence of less active metals
Acidic environments
Areas of mechanical stress
Account for each of these factors that accelerate rust.

## Slide 17: Answers (conditions accelerating rusting)
Salt water is an electrolyte and electrolytes accelerate the redox processes as ions are able to move freely and carry charges that are necessary in redox reactions such as rusting
Impurities can act as the cathode where O2 is reduced readily – Steel is more likely to rust than pure iron
Contact with less active metals such as Cu or Sn means that these less active metals serve as the cathode
Acidic solutions make Fe more soluble
Under stress, individual Fe atoms are less strongly bonded together. This makes it easier for atoms to break away from the crystal lattice as Fe2+ ions