## Slide 1: Water Quality
Criteria
Factors influencing quality

## Slide 2: Why so important?
Water is fixed resource – amount available for use is fixed
Role as solvent (“universal solvent”)
Importance to life

## Slide 3: Factors affecting quality
Water quality determined by:
    Ion concentration
    Dissolved solids
    Hardness
    Turbidity
    Acidity
    Dissolved oxygen
    Biological oxygen demand

## Slide 4: Common ion concentration
Water retains soluble ions it dissolves as it moves through the environment
These include:
  Cations
    typical – Na+, Mg2+, Ca2+, K+, Fe3+
    Heavy metals – e.g. Pb2+, Hg2+, Cd2+, Al3+
  Anions
    Most common - Cl-, SO42-, CO32-, HCO3-, PO43-

## Slide 5: Salinity
Salinity is due to increased concentrations of salts – not necessarily just NaCl
Influence on biological factors – prevents water uptake by plants and direct toxicity in some plants (e.g. Cl-)
Increased concentration = reduced use to humans

## Slide 6: Hardness
Hardness is due to high concentrations of metal ions – particularly Mg2+ & Ca2+
Influences:
  Hampers ability to lather – form suds
  Build-up of deposits in pipes – lime scale
  Reduces life of equipment (e.g. Washer)
  Reduces life of fabrics

## Slide 7: Softening water
The removal of Ca and Mg ions
How is water softened?:
  Ion exchangers - replacing the calcium and magnesium ions in the water with other ions, for instance sodium or potassium
  Distilling
  Boiling followed by settling of the lime Ca(OH)2

## Slide 8: Total Dissolved solids (TDS)
Total Dissolved Solids come from a variety of sources and lead to some typical problems:
  High TDS may effect the aesthetic quality of the water, interfere with washing clothes and corrode plumbing fixtures. For aesthetic reasons, the US EPA established a limit of 500 mg/l, but in general is not a specific health hazard.
  The typical test for TDS is gravimetric, but an approximation can be given by measuring conductivity
Cations combined with carbonates CaCO3, MgCO3 etc | Associated with hardness, scale formation, bitter taste
Cations combined with Chloride NaCl, KCl | Salty or brackish taste, increase corrosivity

## Slide 9: Curing the problem of TDS
Reduction is accomplished by reducing the total amount in the water. This is done during:
  the process of deionization or
  reverse osmosis

## Slide 10: Osmosis and water motion
When two water (or other solvent) volumes are separated by a semi permeable membrane, water will flow from the side of low solute concentration, to the side of high solute concentration

## Slide 11: What’s reverse osmosis?
In reverse osmosis, the idea is to use the membrane to act like an extremely fine filter to create drinkable water from salty (or otherwise contaminated) water.
The salty water is put on one side of the membrane and pressure is applied to stop, and then reverse, the osmotic process

## Slide 12: Turbidity
Turbidity is the amount of particulate matter that is suspended in water – it makes water cloudy
Turbidity measures the scattering effect that suspended solids have on light:
  the greater the scattered light, the higher the turbidity
Drinking water should be less than 5 NTU (Nephelometric Turbidity Units)
In the field, it can be measured using a secchi disk (see diagram left)

## Slide 13: Factors influencing Turbidity
Material that cause water to be turbid include:
  Clay/silt soil erosion
  Algal growth/eutrophication
  finely divided organic and inorganic matter
  Urban run-off
  Waste discharge

## Slide 14: Problems with Turbidity
Turbid water absorbs more heat from the sun, leading to less dissolved O2
Suspended solids in turbid water can clog fish gills, reduce growth rates, decrease resistance to disease, and prevent egg and larval development.
Phytoplankton and fish can be adversely affected by turbidity

## Slide 15: Acidity
Can be influenced by:
  Air pollutants – acid rain
  Leached pollutants from mining sites
  Acid sulfate soils
  Acid rain
Chemicals effecting water acidity include:
  Hydrogen ions
  Dissolved CO2
  Phosphate ions
  Organic acids from decaying organic matter
  H2S

## Slide 16: A bit more …
Increasing alkalinity:
  HCO3-  removes H+ from solution and increases [OH-]
  The build-up of algae also tends to increase the pH of waterways

## Slide 17: Effect of acidity on water quality
Influences biological factors directly – organisms can only survive in narrow pH ranges
Leaching of further ions into solution such as Al3+ which is toxic to many animals

## Slide 18: Dissolved Oxygen
A small amount of oxygen, up to about ten molecules of oxygen per million of water, is actually dissolved in water.
This dissolved oxygen is used by fish and zooplankton during respiration

## Slide 19: BOD
BOD or biochemical oxygen demand is another test of water quality that measures the amount of organic pollution
Organic pollutants consume oxygen when they decompose, so the test involves using aerobic microbes to oxidise (decompose) these pollutants and then comparing the amount of oxygen present before and after.
Greater than 5ppm is polluted

## Slide 20: Factors affecting dissolved oxygen
Rapidly moving water, such as in a mountain stream or large river, tends to contain a lot of dissolved oxygen, while stagnant water contains little
Excess organic material in our lakes and rivers can lower dissolved oxygen concentrations

## Slide 21: Eutrophication
Eutrophication is a process whereby water bodies, such as lakes, estuaries, or slow-moving streams receive excess nutrients that stimulate excessive plant growth
This enhanced plant growth, often called an algal bloom, reduces dissolved oxygen in the water when dead plant material decomposes and can cause other organisms to die.

## Slide 22: Causes of Eutrophication
Natural – very slow
Human influences - accelerated
  add excessive amounts of plant nutrients – phosphates & nitrates from fertilisers increases algal growth
  untreated, or partially-treated, domestic sewage increases algal growth

## Slide 23: Eutrophication explained

## Slide 24: Drinking Water Purification
Natural waters
are filtered
Suspended solids
in water too fine to be filtered
Flocculation: Add alum – KAl(SO4)2 or other flocculant
Settling: Fine particles settle and are removed
by flocculation
Disinfection: Bacterial treatment of water
with chlorine gas or ozone
Fluoride may be added
before pumping to households
Large solids
and
organic matter removed
Flocculated particles settle out to the bottom of the tank as sludge

## Slide 25: Waste Water Purification
Using your text book (pp 280 – 282 of Chemistry Contexts) draw a flow chart to summarise the stages of waste water treatment including:
Primary treatment
Secondary treatment
Tertiary treatment

## Slide 26: Research task
Find out more details about the steps in the process of drinking water purification including the effectiveness of treatments and explain how microscopic membrane filters are designed and how they function